## Slide 1: Finger gesture recognition during hand movement with smart skin technology and deep learning
Presented by: Gal Babayoff & Tomer Roditi Supervised by: Prof. Yael Hanein
Biomedical Engineering Department, Faculty of Engineering, Tel-Aviv University

## Slide 2: Gesture Recognition Aim
Finger gesture recognition has numerous applications in fields such as healthcare, gaming, and robotics.
Smart skin technology and deep learning offer a promising solution over traditional approaches.
Notes: To achieve the most accurate and reliable results
cameras, videos, or gloves.
Electromyography

## Slide 3: WHAT WE ARE WORKING ON THEM US
Expand the work to recognize finger gestures during free movement
sEMG-based finger gesture recognition in a fixed hand position
Notes: This approach expands beyond the previous project, which was limited to static hand positions

## Slide 4: Methods Wireless sEMG system Data collection Data analysis 01 02 03
Notes: composed of three primary components

## Slide 5: Wireless sEMG system
X-trodes Inc. system contains 16 electrodes and a data acquisition unit.
Notes: Nanotechnology
EMG = Electromyography
Bluetooth + sd – sampling rate 4000 kHz

## Slide 6: Data collection
Notes: 2 sessions
4 hand positions
10 gestures
10 repetitions
Total 800 gestures per subject

## Slide 7: Data analysis
Filtering
Features extraction
Segmantion
Model
Notes: Filter – reduce power line interferences and remain within the EMG range.
Segmantaion – into active time windows -> sub windows

## Slide 8: Features extraction
Rms maps of one subject.
Each row represents
one hand gesture, and the columns represent different repetitions of the same gesture.
Notes: Each sub-window: calculate the root-mean-square RMS per channel
Result in heat maps of 16 value (one to each electrode).

## Slide 9: Data analysis
Filtering
Features extraction
Segmantion
Model
Notes: Data pipeline
Model pipeline
Classification tasks

## Slide 10: Model Architecture
Notes: Input size (matches the features map), output size matches the number of classes (different hand gestures)
Batch normalization and drouput layers
Not so deep, not sophisticated! -> Lots of room for improvements as the tasks becomes more complicated

## Slide 11: Classification tasks
Train/test - 80/20 %
accuracy - 95%
2 sessions
3 positions – I,II,III
10 finger gestures
Notes: - Reproducing last year results with the refactored code and simplified pipeline.

## Slide 12: Classification tasks
Train/test - 80/20 %
accuracy - 93%
2 sessions
4 positions – I,II,III,IIII
10 finger gestures
Notes: Adding our new position (moving hand)
Results are pretty much the same, no significant performance degradation.

## Slide 13: Classification tasks
Train/test - 80/20 %
accuracy - 100%
2 sessions
1 position – IIII
10 finger gestures
Notes: - Just to show that the movement of the hand doesn’t affect the quality of the data

## Slide 14: Classification tasks
Train/test – train on session 1, fine tune with 30% of session 2, test on 70% of session 2
accuracy - 90%
2 sessions
4 positions – I,II,III,IIII
10 finger gestures
Notes: - Cross session fast learning
- Improvement from last year, we are using only the same subject data to pretrain the model.

## Slide 15: So Far
Similar achievements in
static positions
model per subject
High accuracy for gentle
Movements

## Slide 16: Future
Collect more data
Develop new pipelines and models for broader movements
Notes: - Need to define a new protocol for data collection with broad hand movements

## Slide 17: Future
Integrate accelerometer data.
Models' architectures.
Static positions collection as a database.
Notes: Transformers architecture
Continuous data segmentation (for online use)

## Slide 18: THANKS

## Slide 19: Loss VS. Accuracy

## Slide 20: Pos |||| signal

## Slide 21: Pos ||| signal